## Slide 1: ERTS Final Assessment – Task 1 (Template)
Jiaxi Han gz20779
Yuhao He kf20807
William Zhang rv20386

## Slide 2: Practical elements
Show that the robot can move around effectively in both modes of operations
Show that you have made use of the LED & Switches
Is there nay difference in operation when you robot works in polling mode and interrupt mode?

## Slide 3: Interrupts
How do you implement operation of robot with polling? Why?
Turn off the interrupt mode service by DisableInterrupt()
Monitor the status of the bumpswitch by using a while loop.
When one of switch pressed, the program will enter a function called checkbumpswitch() to progress corresponding movement.
How do you implement operation of robot with interrupts? Why?
Turn on the interrupt mode service by Enableinterrupt().
Similarly use while loop to run the route, but not to monitor the bumpswitch as the interrupt is registered on the device.
Once one of the bump switches is pressed, an interrupt signal will be sent to microprocessor and device will be immediately stop to run corresponding movement in PORT4_IRQHandler

## Slide 4: Interrupts
How have you kept the ISRs minimal?
ISR overhead can be spilt into fixed part and variable part, while there isn’t much compiler than can handle with fixed overhead as it is associated with the CPU actions. The variable overhead is the time spent on stacking and unstacking the registers used in ISR, which indicates that with more register used by compiler, our time for stacking and unstacking registers increase and this can take a large portion of CPU bandwidth. So in our case, only 6 bump switches will be used.

## Slide 5: Delays
Where have delays been used? Why?
Interrupt: 14 cycles
Polling:217 cycles
We measure the latencies in both modes to compare the time between receiving the request for interrupt and progressing corresponding function in either polling or interrupt modes.
It can be demonstrated that the delays in interrupt mode is much lesser, this is because of logic pattern of interrupt mode that instead of monitoring the whole progress, it only run the interrupt process when a interrupt signal is received.

## Slide 6: CPU Usage
How have you measured the CPU utilization?
 | Interrupt | Polling
No press cycle | 1078212 | 1078290
Pressed cycle | 529396544 | 
CPU utilization | 99.8% |